## Slide 1: Single Writer / Multiple Reader (SWMR)
Dana Robinson
The HDF Group
Efficient Use of HDF5 With High Data Rate X-Ray Detectors
Paul Scherrer Institut

## Slide 2: Basic Idea
Many use cases call for a single writer process which writes data to a single HDF5 file, and multiple readers, which will consume the HDF5 data as it is written.
Ideally, we would like to support this scenario with no communication between the processes.
With no IPC/signals, there are clearly limits on how this can be used. Seeing arbitrary changes in the read files would be expensive. Readers will have to poll for expected changes.
- Changes in dataset sizes
- New groups created in a target group
- etc.

## Slide 3
HDF5 File
Writer
Reader
Reader
Reader
Independent Reader Processes
Data

## Slide 4
HDF5 File
Writer
Reader
Which can then be read by a reader.
With no IPC necessary.
New data elements
Are added to a dataset in the file.
Example

## Slide 5
HDF5 File
Writer
Reader
Reader
Reader
Data
Basic engineering challenge is to ensure that the readers always see a coherent (though possibly not up to date) HDF5 file.
Notes: This is mainly the library's problem so there is very little work for the user to do.

## Slide 6: Setting up for SWMR (Basic)
Very easy to set up!
Writer
- Call H5Fopen or create using the H5F_ACC_SWMR_WRITE flag.
Reader
- Call H5Fopen using the H5F_ACC_SWMR_READ flag.

## Slide 7: Using SWMR (Basic)
Very easy to use!
Writer
- Write data to the HDF5 file.
Reader
- Poll, checking the size of the dataset to see if there is new data
available for reading.
- Read new data, if any.

## Slide 8: Internal Changes
Metadata must be carefully staged so that readers cannot encounter invalid data.
Readers must be more aggressive about discarding their metadata cache entries. This needs to be done after a specified time t.
Readers must make sure that no read operation takes longer than the above time t. (This ensures the reader does not use metadata which has been invalidated by the writer.)
This timeout value t, is stored in the superblock when the file is opened and deleted when the file is closed.

## Slide 9: Metadata Flush Dependencies
1
2
(2)
Suppose we have a metadata item which refers to another metadata item in the file.
metadata
item 1
metadata
item 2
reference to address
of metadata item 2

## Slide 10: Metadata Flush Dependencies
1
2
(3)
If we add a new metadata item to the file and update the reference to point to it, we have to be careful about the order in which the metadata is flushed out of the cache.
metadata
item 1
metadata
item 3
reference to address
of new metadata item 3
3
metadata
item 2

## Slide 11
HDF5 File
Writer
Reader
1
(3)
3
1
(3)
garbage?
2
If the reference-containing item is flushed before the new item, the reader may read the new reference before the item, creating an invalid state.
BAD

## Slide 12
HDF5 File
Writer
Reader
1
(3)
3
1
(2)
2
If the new metadata item is flushed before the reference-containing item, the reader will not be fully up to date, but will still be consistent.
3
OK

## Slide 13
HDF5 File
Writer
Reader
1
(3)
3
1
(2)
2
We are creating flush dependencies in the internal data structures to ensure that metadata cache flush operations occur in the proper order.
3
OK

## Slide 14: File Open and Close Problem
The writer MUST be the first process to open the file so the superblock message can be written.
If a reader opens the file first, it will find no SWMR superblock message and not use any SWMR protocols when accessing the file.
Alternatively, we can create a mechanism for communicating SWMR on/off between processes.

## Slide 15: File Open and Close Problem
Possible solution:
Consider the superblock as volatile whenever SWMR is a possibility.
Requires setting a SWMR timeout t.
- Writers do not write until time t has passed.
- Readers check for SWMR superblock msg every time t.
Ensures that the reader and writer will use SWMR together.
Also allows readers to discontinue using SWMR protocols when the writer is not actively writing (performance enhancement).
Notes: File system delays mean that the writer may have to wait some small multiple of t

## Slide 16: Status
Scheduled HDF5 1.10.0 feature.
Being paid for by a commercial client of The HDF Group.
Currently under development.
Metadata cache flush dependencies in progress.
Other work in the design stage.
Very high priority.