## Slide 1
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper
“All processes write to all dsets (N processes / 50 dsets ) ” on CONTIG dsets
Performance tests : Dim 128000, CONTIG, 0.5MB each dset, (on Hopper )’ Test: all processes write to all datasets. NEW |  |  |  | 
#dsets |  | H5Dwrite() (COLL – loop) | H5Dwrite_multi() | Increased Performance Rate
24 procs 50 Dsets | WRITE raw only | 64.166 sec | 0.424 – 1.160 sec | 55 times
 | Fclose | 0.005 – 0.765 sec | 0.005 – 0.006 sec | 
 | Overall | 65.480 sec | 2.478 sec | 26 times
48 procs 50 Dsets | WRITE raw only | 74.236 sec | 0.352 – 1.103 sec | 67 times
 | Fclose | 0.042 – 5.779 sec | 0.069 – 0.070 sec | 
 | Overall | 76.825 sec | 3.485 sec | 22 times
96 procs 50 Dsets | WRITE raw only | 254.081 sec | 0.664 – 5.099 sec | 50 times
 | Fclose | 0.396 – 6.133 sec | 0.071 - 0.072 sec | 
 | Overall | 262.008 sec | 7.354 sec | 36times
128 procs 50 Dsets | WRITE raw only | 281.438 Sec | 0.589 – 6.333 sec | 44 times
 | Fclose | 0.699 – 1.474 sec | 0.682 – 0.683 sec | 
 | Overall | 285 sec | 9.311 sec | 30 times
256 procs 50 Dsets | WRITE raw only | 492.256 Sec | 0.633 – 8.385 sec | 59 times
 | Fclose | 1.332 – 12.087 sec | 1.303 – 1.305 sec | 
 | Overall | 501 sec | 12.108 sec | 41 times
Note: “Overall” mean elapsed time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)

## Slide 2
Chart: Number of processes
| 24 | 48 | 96 | 128 | 256
H5Dwrite | 64.166 | 74.236 | 254.081 | 281.438 | 492.256
H5Dwrite_multi | 1.16 | 1.103 | 5.099 | 6.333 | 8.385
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper
“All processes write to all dsets (N processes / 50 dsets ) ” on CONTIG dsets

## Slide 3
Note: “Overall” mean elapsed time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper
“All processes write to all dsets (N processes / 30 dsets ) ” on CHUNKED (/10)
Performance tests : Dim 128000, 10 CHUNKED, 0.5MB each dset, (on Hopper )’ Test: all processes write to all datasets. NEW |  |  |  | 
#dsets |  | H5Dwrite() (COLL – loop) | H5Dwrite_multi() | Increased Performance Rate
24 procs 30 Dsets | WRITE raw only | 58.565 sec | 0.083 – 0.835 sec | 70 times
 | Fclose | 0.006 – 0.755 Sec | 0.005 – 0.006 sec | 
 | Overall | 59.847 sec | 2.095 sec | 28 times
48 procs 30 Dsets | WRITE raw only | 78.273 sec | 0.338 – 1.077 sec | 72 times
 | Fclose | 0.060 – 0.819 –sec | 0.086 – 0.087 sec | 
 | Overall | 80.773 sec | 3.456 sec | 23 times
96 procs 30 Dsets | WRITE raw only | 158.507 sec | 0.742 – 3.495 sec | 45 times
 | Fclose | 0.051 – 10.798 sec | 0.302 – 0.303 sec | 
 | Overall | 160.877 sec | 7.016 sec | 22 times
128 procs 30 Dsets | WRITE raw only | 187.997 Sec | 0.662 – 6.414 sec | 29 times
 | Fclose | 0.655 – 1.419 sec | 0.650 – 0.650 sec | 
 | Overall | 191.646 sec | 9.391 sec | 20 times
256 procs 30 Dsets | WRITE raw only | 412.168 Sec | 0.718 – 8.474 sec | 48 times
 | Fclose | 1.331 – 7.794 sec | 1.296 – 1.297 sec | 
 | Overall | 418.000 sec | 13.321 sec | 31 times

## Slide 4
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper
“All processes write to all dsets (N processes / 30 dsets ) ” on CHUNKED (/10)
Chart: Number of processes
| 24 | 48 | 96 | 128 | 255
H5Dwrite | 58.565 | 78.273 | 158.507 | 187.997 | 412.168
H5Dwrite_multi | 0.835 | 1.077 | 3.495 | 6.414 | 8.474

## Slide 5
Note: “Overall” mean elapse dtime of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper
“Embarrassingly Parallel test (N processes /dsets pair) ” on CONTIG dsets
Performance tests : Dim 256000, CONTIG, 1MB each dset, Float type, (on Hopper ) Test proc-dset pair IO. ‘embarrassingly parallel’ vs ‘multi_dset’ |  |  |  | 
#dsets |  | H5Dwrite() (embarrassing para) | H5Dwrite_multi() | Increased Performance Rate
24 procs 24 dsets (24MB) | WRITE raw only | sec | sec | 
 | Overall | 02.44 sec | 02.47 sec | 
48 procs 48 dsets (48MB) | WRITE raw only | sec | sec | 
 | Fclose |  |  | 
 | Overall | 03.94 sec | 04.11 sec | 
96 procs 96 dsets (96MB) | WRITE raw only | 0.360 sec | 0.254 sec | 
 | Fclose | sec | sec | 
 | Overall | 04.39 sec | 04.81 sec | 
128 procs 128 dsets (128MB) | WRITE raw only | 0.326 Sec | 0.875 sec | 
 | Fclose | 7.041 sec | 6.837 sec | 
 | Overall | 0:09.76 sec | 0:10.52 sec | 
256 procs 256 dsets (256MB) | WRITE raw only | Xx sec | 0.185 sec | 
 | Fclose | 13.454 sec | 13.436 sec | 
 | Overall | 0:16.34 sec | 0:17.42 sec | 

## Slide 6
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper
“Embarrassingly Parallel test (N processes /dsets pair) ” on CONTIG dsets
Chart: Number of processes & contig datasets
| 24 | 48 | 96 | 128 | 256
H5Dwrite | 2.44 | 3.94 | 4.39 | 7.04 | 13.554
H5Dwrite_multi | 2.47 | 4.11 | 4.81 | 6.837 | 13.436

## Slide 7
Note: “Overall” mean elapsed time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper
“Embarrassingly Parallel test (N processes /dsets pair) ” on CHUNKED dsets
Performance tests : Dim 256000, CHUNKED 25600, 1MB each dset, Float type, (on Hopper ) Test proc-dset pair IO. ‘embarrassingly parallel’ vs ‘multi_dset’ |  |  |  | 
#dsets |  | H5Dwrite() (embarrassing para) | H5Dwrite_multi() | Increased Performance Rate
24 procs 24 dsets (24MB) | WRITE raw only | sec | sec | 
 | Fclose | sec | sec | 
 | Overall | 2.86 sec | 2.460sec | 
48 procs 48 dsets (48MB) | WRITE raw only | sec | sec | 
 | Fclose | sec | sec | 
 | Overall | 3.846 sec | 3.780 sec | 
96 procs 96 dsets (96MB) | WRITE raw only | sec | sec | 
 | Fclose | sec | sec | 
 | Overall | 5.33 sec | 5.31 sec | 
128 procs 128 dsets (128MB) | WRITE raw only | Sec | sec | 
 | Fclose | sec | sec | 
 | Overall | 11.34 sec | 10.75 sec | 
256 procs 256 dsets (256MB) | WRITE raw only | sec | sec | 
 | Fclose | sec | sec | 
 | Overall | 18.460 sec | 17.067 sec | 

## Slide 8
Chart: Number of processes & chunked datasets
| 24 | 48 | 96 | 128 | 255
H5Dwrite | 2.68 | 3.846 | 5.33 | 11.34 | 18.46
H5Dwrite_multi | 2.46 | 3.78 | 5.31 | 10.75 | 17.067
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper
“Embarrassingly Parallel test (N processes /dsets pair) ” on CHUNKED dsets

## Slide 9
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper OLD
“All processes write to all dsets (N processes / 55 dsets ) ” on CONTIG dsets
Note: “Overall” mean elapse time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)
Performance tests : Dim 128000, CONTIG, 0.5MB each dset, Float type, (on Hopper )’ Test: all processes write to all datasets. |  |  |  | 
#dsets |  | H5Dwrite() (COLL – loop) | H5Dwrite_multi() | Increased Performance Rate
24 procs 55 Dsets | WRITE raw only | 63.054 sec | 0.786 sec | 
 | Fclose | 0.012 sec | 0.390 sec | 
 | Overall | 64.857s sec | 2.788 sec | 23 times
48 procs 55 Dsets | WRITE raw only | 98.185 sec | 0.866 sec | 
 | Fclose | 0.097 sec | 0.539 sec | 
 | Overall | 100.844 sec | 3.919 sec | 25 times
64 procs 55 Dsets | WRITE raw only | 195.563 sec | 0.382 sec | 
 | Fclose | 0.735 sec | 4.029 sec | 
 | Overall | 198.901 sec | 6.952 sec | 28 times
96 procs 55 Dsets | WRITE raw only | 272.803 sec | 0.872 sec | 
 | Fclose | 0.765 sec | 5.835 sec | 
 | Overall | 276.387 sec | 9.330 sec | 29 times
128 procs 55 Dsets | WRITE raw only | 347.788 Sec | 0.910 sec | 
 | Fclose | 11.217 sec | 7.198 sec | 
 | Overall | 364.659 sec | 10.533 sec | 35 times
256 procs 55 Dsets | WRITE raw only | 567.086 sec | 0.747 sec | 
 | Fclose | 11.568 sec | 11.916 sec | 
 | Overall | 581.345 sec | 15.603 sec | 37 times

## Slide 10
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper OLD
“All processes write to all dsets (N processes / 55 dsets ) ” on CONTIG dsets
Chart: Number of processes
| 24 | 48 | 96 | 128 | 256
H5Dwrite | 64.166 | 74.236 | 254.081 | 281.438 | 492.256
H5Dwrite_multi | 1.16 | 1.103 | 5.099 | 6.333 | 8.385

## Slide 12
Note: “Overall” mean elapse time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper (1 process, 1 node )
CHUNKED Datasets (1MB per dataset)
Performance tests : Dim 256000, CHUNK 25600, 1MB each dset , Float type (on Hopper – 1process,1node) |  |  |  | 
#dsets |  | H5Dwrite() | H5Dwrite_multi() | Increased Performance Rate
200 Dsets (200MB) | WRITE raw only | 6.417 sec | 0.598 sec | 1,073% (10times)
 | Overall | 0:09.21 sec | 0:02.64 sec | 
400 Dsets (400MB) | WRITE raw only | 12.238 sec | 1.190 sec | 1,028%
 | Overall | 0:15.66 sec | 0:03.69 sec | 
800 Dsets (800 MB) | WRITE raw only | 30.283 sec | 3.116 sec | 972%
 | Overall | 0:33.09 sec | 0:08.51 sec | 
1200 Dsets (1.2GB) | WRITE raw only | 55.248 sec | 4.738 sec | 1,166%
 | Overall | 00:57.85 sec | 0:11.93 sec | 
1600 Dsets (1.6GB) | WRITE raw only | 60.295 sec | 7.507 sec | 803%
 | Overall | 1:04.89 sec | 0:15.87 sec | 

## Slide 13
Chart: Number of Chunked datasets
| 200 | 400 | 800 | 1200 | 1600
H5Dwrite | 6.417 | 12.238 | 30.283 | 55.248 | 60.295
H5Dwrite_multi | 0.598 | 1.19 | 3.116 | 4.738 | 7.507

## Slide 14
Note: “Overall” mean elapse time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper (1 process, 1 node )
CHUNKED Datasets (1MB per dataset)
Performance tests : Dim 256000, CONTIG, 1MB each dset, Float type, (on Hopper – 1process, 1node) |  |  |  | 
#dsets |  | H5Dwrite() | H5Dwrite_multi() | Increased Performance Rate
400 Dsets (400MB) | WRITE raw only | 12.837 sec | 1.504 sec | 845%
 | Overall | 0:15.33 sec | 0:02.92 sec | 
800 Dsets (800MB) | WRITE raw only | 26.143 sec | 2.680 sec | 975%
 | Overall | 0:28.44 sec | 0:04.29 sec | 
1200 Dsets (1.2GB) | WRITE raw only | 39.429 sec | 3.371 sec | 1,170%
 | Overall | 0:42.58 sec | 0:05.78 sec | 
1600 Dsets (1.6GB) | WRITE raw only | 53.239 sec | 4.926 sec | 1,080%
 | Overall | 0:54.25 sec | 0:06.92 sec | 
2000 Dsets (2GB) | WRITE raw only | 69.818 sec | 6.023 sec | 1,160%
 | Overall | 1:10.51 sec | 0:08.16 sec | 

## Slide 15
Chart: Number of Contig datasets
| 400 | 800 | 1200 | 1600 | 2000
H5Dwrite | 12.837 | 26.143 | 39.429 | 53.239 | 69.818
H5Dwrite_multi | 1.504 | 2.68 | 3.371 | 4.926 | 6.023

## Slide 16
Performance tests : Dim 200, CHUNK 20 , Float type (on Hopper – 1process,1node) |  |  |  | 
#dsets |  | H5Dwrite() | H5Dwrite_multi() | Increased Performance Rate
50 Dsets | WRITE raw only | 1.585 sec | 0.040 sec | 40 times
 | Overall | 0:02.55 sec | 0:01.04 sec | 
100 Dsets | WRITE raw only | 3.172 sec | 0.060 sec | 52 times
 | Overall | 0:04.13 sec | 0:01.07 sec | 
200 Dsets | WRITE raw only | 6.340 sec | 0.105 sec | 60 times
 | Overall | 0:07.43 sec | 0:01.11 sec | 
400 Dsets | WRITE raw only | 12.682 sec | 0.231 sec | 55 times
 | Overall | 0:13.86 sec | 0:01.34 sec | 
800 Dsets | WRITE raw only | 25.335 sec | 0.688 sec | 37 times
 | Overall | 0:26.68 sec | 0:02.11 sec | 
Note: “Overall” mean elapse time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper (1 process, 1 node )
CHUNKED Datasets

## Slide 17
Chart: Number of Chunked datasets
| 50 | 100 | 200 | 400 | 800
H5Dwrite | 1.585 | 3.172 | 6.34 | 12.682 | 25.335
H5Dwrite_multi | 0.04 | 0.06 | 0.105 | 0.231 | 0.688

## Slide 18
Performance tests : Dim 200, CONTIG , Float type (on Hopper – 1process, 1node) |  |  |  | 
#dsets |  | H5Dwrite() | H5Dwrite_multi() | Increased Performance Rate
400 Dsets | WRITE raw only | 12.758 sec | 0.040 sec | 318 times
 | Overall | 0:13.78 sec | 0:01.73 sec | 
800 Dsets | WRITE raw only | 25.506 sec | 0.048 sec | 531 times
 | Overall | 0:26.75 sec | 0:01.20 sec | 
1600 Dsets | WRITE raw only | 51.531 sec | 0.101 sec | 510 times
 | Overall | 0:52.85 sec | 0:01.21 sec | 
3200 Dsets | WRITE raw only | 111.702 sec | 0.165 sec | 676 times
 | Overall | 1:53.24 sec | 0:01.61 sec | 
6400 Dset | WRITE raw only | 213.560 sec | 0.252 sec | 802 times
 | Overall | 3:35.67 sec | 0:02.03 sec | 
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper (1 process, 1 node )
CONTIGUOUS Datasets
Note: “Overall” mean elapse time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)

## Slide 19
Chart: Number of Contig datasets
| 400 | 800 | 1600 | 3200 | 6400
H5Dwrite | 12.758 | 25.506 | 51.531 | 111.702 | 213.56
H5Dwrite_multi | 0.04 | 0.048 | 0.101 | 0.165 | 0.252

## Slide 20
Performance tests : Dim 200, CHUNK 20 , Float type ( on Hopper – 6processes (2process each over 3node)) |  |  |  | 
#dsets |  | H5Dwrite() | H5Dwrite_multi() | Increased Performance Rate
50 Dsets | WRITE raw only | 9.870 - 19.292 sec | 0.044 - 0.081 sec | 224 - 238 times
 | Overall | 0:35.45 sec | 0:01.35 sec | 
100 Dsets | WRITE raw only | 22.620 - 46.939 sec | 0.082 - 0.115 sec | 275 - 408 times
 | Overall | 1:08.35 sec | 0:02.15 sec | 
200 Dsets | WRITE raw only | 34.187 - 80.319 sec | 0.108 - 0.141sec | 316 - 569 times
 | Overall | 2:15.05 sec | 0:01.64 sec | 
400 Dsets | WRITE raw only | 82.837 - 171.793 sec | 0.259 - 0.296 sec | 319 - 580 times
 | Overall | 4:31.32 sec | 0:01.80 sec | 
800 Dsets | WRITE raw only | 154.203 - 272.157 sec | 0.858 - 0.934 sec | 180 - 291 times
 | Overall | 6:32.83 sec | 0:03.36 sec | 
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper (6 processes , 3 nodes 2processes each)
CHUNKED Datasets
Note: “Overall” mean elapse time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)
The results from H5Dwrite() seems much slower , probably because memory and file spaces are selected all per process IO., thus each process perform write IO redundantly.

## Slide 21
Chart: Number of Chunked datasets
| 50 | 100 | 200 | 400 | 800
H5Dwrite | 19.292 | 46.939 | 80.319 | 171.793 | 272.157
H5Dwrite_multi | 0.081 | 0.115 | 0.141 | 0.296 | 0.934

## Slide 22
Performance tests : Dim 200, CONTIG , Float type ( on Hopper – 6processes (2process each over 3node)) |  |  |  | 
#dsets |  | H5Dwrite() | H5Dwrite_multi() | Increased Performance Rate
400 Dsets | WRITE raw only | 26.716 - 31.684 sec | 0.043 - 0.086 sec | 368 - 621 times
 | Overall | 0:33.19 sec | 0:01.47 sec | 
800 Dsets | WRITE raw only | 51.623 - 51.728 sec | 0.058 - 0.111 sec | 466 - 890 times
 | Overall | 0:53.41 sec | 0:01.59 sec | 
1600 Dsets | WRITE raw only | 110.794 - 111.280 sec | 0.085 - 0.135 sec | 824 – 1303 times
 | Overall | 1:58.09 sec | 0:01.71 sec | 
3200 Dsets | WRITE raw only | 213.682 - 223.493 sec | 0.133 - 0.181 sec | 1234 - 1606 times
 | Overall | 3:45.76 sec | 0:02.01 sec | 
6400 Dset | WRITE raw only | 424.471 - 429.848 sec | 0.589 - 0.625 sec | 687 - 720 times
 | Overall | 7:18.95 sec | 0:02.97 sec | 
Performance Comparison between H5Dwrite_multi and H5Dwrite on NERSC Hopper (6 processes , 3 nodes 2processes each)
CONTIGUOUS Datasets
Note: “Overall” mean elapse time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)
The results from H5Dwrite() seems much slower , probably because memory and file spaces are selected all per process IO., thus each process perform write IO redundantly.

## Slide 23
Chart: Number of Contig datasets
| 400 | 800 | 1600 | 3200 | 6400
H5Dwrite | 31.684 | 51.728 | 111.28 | 223.493 | 429.848
H5Dwrite_multi | 0.086 | 0.111 | 0.135 | 0.181 | 0.625

## Slide 24
Performance tests : Dim 200, CONTIG , Float type (on Wallaby) |  |  |  | 
#dsets |  | H5Dwrite() | H5Dwrite_multi() | Increased Performance Rate
400 Dsets | WRITE raw only | 0.456 sec | 0.111 sec | 410%
 | Overall | real 0m0.957s user 0m0.160s sys 0m0.103s | real 0m0.746s user 0m0.142s sys 0m0.085s | 132%
800 Dsets | WRITE raw only | 0.901 sec | 0.051 sec | 1800%
 | Overall | real 0m2.004s user 0m0.303s sys 0m0.261s | real 0m1.408s user 0m0.311s sys 0m0.143s | 142%
1600 Dsets | WRITE raw only | 1.773 sec | 0.098 sec | 1809%
 | Overall | real 0m3.938s user 0m0.663s sys 0m0.550s | real 0m2.562s user 0m0.608s sys 0m0.291s | 153%
3200 Dsets | WRITE raw only | 3.425 sec | 0.176 sec | 1946%
 | Overall | real 0m7.702s user 0m1.210s sys 0m1.174s | real 0m4.947s user 0m1.183s sys 0m0.526s | 155%
6400 Dset | WRITE raw only | 7.704 sec | 0.632 sec | 1218%
 | Overall | real 0m17.170s user 0m2.599s sys 0m2.057s | real 0m9.760s user 0m2.463s sys 0m1.063s | 175%
Performance Table – Multiple Contiguous Datasets Write comparison
Note: “Overall” mean elapse time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)

## Slide 25
Chart: Number of datasets
| 400 | 800 | 1600 | 3200 | 6400
H5Dwrite | 0.456 | 0.901 | 1.773 | 3.425 | 7.704
H5Dwrite_multi | 0.111 | 0.051 | 0.098 | 0.176 | 0.632
Performance Chart – Multiple Contiguous Datasets Write comparison

## Slide 26
Performance tests : Dim 200, CHUNK 20 , Float type (on Wallaby) |  |  |  | 
#dsets |  | H5Dwrite() | H5Dwrite_multi() | Increased Performance Rate
50 Dsets | WRITE raw only | 0.555 sec | 0.076 sec | 730%
 | Overall | real 0m1.181s user 0m0.067s sys 0m0.191s | real 0m0.824s user 0m0.068s sys 0m0.088s | 135%
100 Dsets | WRITE raw only | 1.077 sec | 0.046 sec | 2340%
 | Overall | real 0m2.478s user 0m0.129s sys 0m0.356s | real 0m1.180s user 0m0.074s sys 0m0.119s | 210%
200 Dsets | WRITE raw only | 2.103 sec | 0.143 sec | 1470%
 | Overall | real 0m4.792s user 0m0.229s sys 0m0.529s | real 0m2.831s user 0m0.243s sys 0m0.316s | 170%
400 Dsets | WRITE raw only | 4.246 sec | 0.291 sec | 1460%
 | Overall | real 0m9.711s user 0m0.455s sys 0m1.017s | real 0m5.522s user 0m0.489s sys 0m0.615s | 175%
800 Dsets | WRITE raw only | 8.340 sec | 1.018 | 820%
 | Overall | real 0m18.768s user 0m0.848s sys 0m2.299s | real 0m11.344s user 0m1.399s sys 0m1.393s | 166%
Performance Table – Multiple Chunked Datasets Write comparison
(dataset dim size 200 / chunk dim size 20)
Note: “Overall” mean elapse time of application from begin to end. (thus include H5Fopen, H5Fclose, H5Dcreat, H5Dclose , etc ..)

## Slide 27
Chart: Number of datasets
| 50 | 100 | 200 | 400 | 800
H5Dwrite | 0.555 | 1.077 | 2.103 | 4.246 | 8.34
H5Dwrite_multi | 0.076 | 0.046 | 0.143 | 0.291 | 1.018
Performance Chart – Multiple Chunked Datasets Write comparison
(dataset dim size 200 / chunk dim size 20)